All Set Input commands for the 8x1 VGA Switch start with

09 53 57 90 08 FF 02

Then comes the port, 01 to 08

so assuming we are switch to port 4 the command would be

09 53 57 90 08 FF 02 04

Then comes the last hex number which is the sum of all hex numbers,

the sum of all numbers but the port is 4C and the port in this case is 04 which equals to 50

The final command line is

09 53 57 90 08 FF 02 04 50

The commands for all ports

Port 1

09 53 57 90 08 FF 02 01 4D

Port 2

09 53 57 90 08 FF 02 02 4E

Port 3

09 53 57 90 08 FF 02 03 4F

Port 4

09 53 57 90 08 FF 02 04 50

Port 5

09 53 57 90 08 FF 02 05 51

Port 6

09 53 57 90 08 FF 02 06 52

Port 7

09 53 57 90 08 FF 02 07 53

Port 8

09 53 57 90 08 FF 02 08 54